## Slide 1
Ansys Fluent Simulation Report

## Slide 2: Header
Analyst | HenriqueResende
Date | 10/20/2024 11:21 PM
Table of contents

## Slide 3: Table of Contents
System Information
Geometry and Mesh
  Mesh Size
  Mesh Quality
  Orthogonal Quality
Simulation Setup
  Physics
    Models
    Material Properties
    Cell Zone Conditions
    Boundary Conditions
    Reference Values
  Solver Settings
Run Information
Solution Status
Report Definitions
Plots
  Residuals
  Report Plots

## Slide 4: System Information
Application | Fluent
Settings | 3d, double precision, pressure-based, standard k-epsilon
Version | 24.2.0-10192
Source Revision | 149ed7492d
Build Time | May 13 2024 11:22:47 EST
CPU | 13th Gen Intel(R) Core(TM) i9-13900HX
OS | Windows
Table of contents
System Information

## Slide 5
Table of contents
Geometry and Mesh
Geometry and Mesh

## Slide 6: Mesh Size
Cells | Faces | Nodes
100244 | 551511 | 401849
Table of contents
Geometry and Mesh / Mesh Size

## Slide 7: Mesh Quality
Name | Type | Min Orthogonal Quality | Max Aspect Ratio
solid | Poly Cell | 0.33035286 | 14.419191
Table of contents
Geometry and Mesh / Mesh Quality

## Slide 8: Orthogonal Quality
Table of contents
Geometry and Mesh / Orthogonal Quality

## Slide 9
Table of contents
Simulation Setup
Simulation Setup

## Slide 10
Table of contents
Simulation Setup / Physics
Physics

## Slide 11: Models
Model | Settings
Space | 3D
Time | Steady
Viscous | Standard k-epsilon turbulence model
Wall Treatment | Standard Wall Functions
Heat Transfer | Enabled
Table of contents
Simulation Setup / Physics / Models

## Slide 12: Material Properties
- Fluid | 
- air | 
Density | 1.225 kg/m^3
Cp (Specific Heat) | 1006.43 J/(kg K)
Thermal Conductivity | 0.0242 W/(m K)
Viscosity | 1.7894e-05 kg/(m s)
Molecular Weight | 28.966 kg/kmol
- Solid | 
- aluminum | 
Density | 2719 kg/m^3
Cp (Specific Heat) | 871 J/(kg K)
Thermal Conductivity | 202.4 W/(m K)
Table of contents
Simulation Setup / Physics / Material Properties

## Slide 13: Cell Zone Conditions
- Fluid | 
- solid | 
Material Name | air
Specify source terms? | no
Specify fixed values? | no
Frame Motion? | no
Laminar zone? | no
Porous zone? | no
3D Fan Zone? | no
Table of contents
Simulation Setup / Physics / Cell Zone Conditions

## Slide 14: Boundary Conditions
- Inlet | 
- inlet_b | 
Velocity Specification Method | Magnitude, Normal to Boundary
Reference Frame | Absolute
Velocity Magnitude [m/s] | 5
Supersonic/Initial Gauge Pressure [Pa] | 0
Temperature [K] | 298.15
Turbulence Specification Method | Intensity and Viscosity Ratio
Turbulent Intensity [%] | 5
Turbulent Viscosity Ratio | 10
- inlet_a | 
Velocity Specification Method | Magnitude, Normal to Boundary
Reference Frame | Absolute
Table of contents
Simulation Setup / Physics / Boundary Conditions (1 of 4)

## Slide 15: Boundary Conditions
Velocity Magnitude [m/s] | 10
Supersonic/Initial Gauge Pressure [Pa] | 0
Temperature [K] | 323.15
Turbulence Specification Method | Intensity and Viscosity Ratio
Turbulent Intensity [%] | 5
Turbulent Viscosity Ratio | 10
- Outlet | 
- outlet | 
Gauge Pressure [Pa] | 0
Pressure Profile Multiplier | 1
Build artificial walls to prevent reverse flow? | yes
Radial Equilibrium Pressure Distribution | no
Average Pressure Specification? | no
Table of contents
Simulation Setup / Physics / Boundary Conditions (2 of 4)

## Slide 16: Boundary Conditions
Specify targeted mass flow rate | no
- Symmetry | 
symmetry_1 | symmetry
symmetry_2 | symmetry
- Wall | 
- wall | 
Wall Thickness [m] | 0
Heat Generation Rate [W/m^3] | 0
Material Name | aluminum
Thermal BC Type | Heat Flux
Heat Flux [W/m^2] | 0
Enable shell conduction? | no
Wall Motion | Stationary Wall
Table of contents
Simulation Setup / Physics / Boundary Conditions (3 of 4)

## Slide 17: Boundary Conditions
Shear Boundary Condition | No Slip
Wall Roughness Height [m] | 0
Wall Roughness Constant | 0.5
Convective Augmentation Factor | 1
Table of contents
Simulation Setup / Physics / Boundary Conditions (4 of 4)

## Slide 18: Reference Values
Area | 1 m^2
Density | 1.225 kg/m^3
Enthalpy | 0 J/kg
Length | 1 m
Pressure | 0 Pa
Temperature | 288.16 K
Velocity | 1 m/s
Viscosity | 1.7894e-05 kg/(m s)
Ratio of Specific Heats | 1.4
Yplus for Heat Tran. Coef. | 300
Reference Zone | solid
Table of contents
Simulation Setup / Physics / Reference Values

## Slide 19: Solver Settings
- Equations | 
Flow | True
Turbulence | True
Energy | True
- Numerics | 
Absolute Velocity Formulation | True
- Pseudo Time Explicit Relaxation Factors | 
Density | 1
Body Forces | 1
Turbulent Kinetic Energy | 0.75
Turbulent Dissipation Rate | 0.75
Turbulent Viscosity | 1
Energy | 0.75
Table of contents
Simulation Setup / Solver Settings (1 of 3)

## Slide 20: Solver Settings
Explicit Momentum | 0.5
Explicit Pressure | 0.5
- Pressure-Velocity Coupling | 
Type | Coupled
Pseudo Time Method (Global Time Step) | True
- Discretization Scheme | 
Pressure | Second Order
Momentum | Second Order Upwind
Turbulent Kinetic Energy | First Order Upwind
Turbulent Dissipation Rate | First Order Upwind
Energy | Second Order Upwind
- Solution Limits | 
Minimum Absolute Pressure [Pa] | 1
Table of contents
Simulation Setup / Solver Settings (2 of 3)

## Slide 21: Solver Settings
Maximum Absolute Pressure [Pa] | 5e+10
Minimum Static Temperature [K] | 1
Maximum Static Temperature [K] | 5000
Minimum Turb. Kinetic Energy [m^2/s^2] | 1e-14
Minimum Turb. Dissipation Rate [m^2/s^3] | 1e-20
Maximum Turb. Viscosity Ratio | 100000
Table of contents
Simulation Setup / Solver Settings (3 of 3)

## Slide 22: Run Information
Number of Machines | 1
Number of Cores | 4
Case Read | 13.328 seconds
Iteration | 58.86 seconds
AMG | 44.847 seconds
Virtual Current Memory | 1.81635 GB
Virtual Peak Memory | 1.83583 GB
Memory Per M Cell | 11.906
Table of contents
Run Information

## Slide 23: Solution Status Iterations: 155
 | Value | Absolute Criteria | Convergence Status
continuity | 9.33096e-07 | 1e-06 | Converged
x-velocity | 1.502658e-10 | 1e-06 | Converged
y-velocity | 1.385655e-09 | 1e-06 | Converged
z-velocity | 1.47866e-08 | 1e-06 | Converged
energy | 1.481312e-09 | 1e-06 | Converged
k | 2.053712e-07 | 1e-06 | Converged
epsilon | 2.75185e-07 | 1e-06 | Converged
Table of contents
Solution Status

## Slide 24: Report Definitions
max_velocity | 20.98137 | m/s
outlet_velocity | 15.00056 | m/s
outlet_flow_rate | -0.00275625 | kg/s
inlet_b_flow_rate | 0.00091875 | kg/s
inlet_a_flow_rate | 0.0018375 | kg/s
pressure_outlet | 147.1982 | Pa
pressure_inlet_b | 174.4059 | Pa
pressure_inlet_a | 217.8503 | Pa
force_z | 0.002278075 | N
force_y | -0.02871437 | N
force_x | 9.113515e-08 | N
outlet_temp | 313.4944 | K
mass_flow_rate | 7.422899e-11 | kg/s
Table of contents
Report Definitions

## Slide 25
Table of contents
Plots
Plots

## Slide 26: Residuals
Chart: Residuals
Table of contents
Plots / Residuals

## Slide 27
Table of contents
Plots / Report Plots
Report Plots

## Slide 28: report-def-0-rplot
Chart: report-def-0-rplot
Table of contents
Plots / Report Plots / report-def-0-rplot

## Slide 29: outlet_temp-rplot
Chart: outlet_temp-rplot
Table of contents
Plots / Report Plots / outlet_temp-rplot

## Slide 30: force_x-rplot
Chart: force_x-rplot
Table of contents
Plots / Report Plots / force_x-rplot

## Slide 31: force_y-rplot
Chart: force_y-rplot
Table of contents
Plots / Report Plots / force_y-rplot

## Slide 32: force_z-rplot
Chart: force_z-rplot
Table of contents
Plots / Report Plots / force_z-rplot

## Slide 33: pressure_inlet_a-rplot
Chart: pressure_inlet_a-rplot
Table of contents
Plots / Report Plots / pressure_inlet_a-rplot

## Slide 34: pressure_inlet_b-rplot
Chart: pressure_inlet_b-rplot
Table of contents
Plots / Report Plots / pressure_inlet_b-rplot

## Slide 35: pressure_outlet-rplot
Chart: pressure_outlet-rplot
Table of contents
Plots / Report Plots / pressure_outlet-rplot

## Slide 36: inlet_a_flow_rate-rplot
Chart: inlet_a_flow_rate-rplot
Table of contents
Plots / Report Plots / inlet_a_flow_rate-rplot

## Slide 37: inlet_b_flow_rate-rplot
Chart: inlet_b_flow_rate-rplot
Table of contents
Plots / Report Plots / inlet_b_flow_rate-rplot

## Slide 38: outlet_flow_rate-rplot
Chart: outlet_flow_rate-rplot
Table of contents
Plots / Report Plots / outlet_flow_rate-rplot

## Slide 39: outlet_velocity-rplot
Chart: outlet_velocity-rplot
Table of contents
Plots / Report Plots / outlet_velocity-rplot

## Slide 40: max_velocity-rplot
Chart: max_velocity-rplot
Table of contents
Plots / Report Plots / max_velocity-rplot